|  | Mnemonics | I/D Bus OP Code Hex & Binary | Name (Execution cycles) | Symbolic Equation |
| --- | --- | --- | --- | --- |
| ARITHMETIC INSTRUCTIONS | AD | 0B 0000 1011 | Add (1) | C, A ( A + M |
|  | ADC | 0A 0000 1010 | Add with carry-in (1) | C, A ( A + M + C |
|  | ADSK | 09 0000 1001 | Add and skip on carry-out (1) | C, A ( A + M Skip if C = 1 |
|  | ADCSK | 08 0000 1000 | Add with carry-in and skip on carry-out (1) | C, A ( A + M + C Skip if C = 1 |
|  | ADI | 60 – 6E 0110 xxxx | Add immediate and skip on carry-out (1) | C, A ( A + [I(4:1)] Skip if C = 1 |
|  | DC | 65 0110 0101 | Decimal Correction (1) | A ( A + 1010 |
| LOGICAL INSTRUCTIONS | AND | 0D 0000 1101 | Logical AND (1) | A ( A ( M |
|  | OR | 0F 0000 1111 | Logical OR (1) | A ( A ( M |
|  | EOR | 0C 0000 1100 | Logical Exclusive-OR (1) | A ( A ( M |
|  | COMP | 0E 0000 1110 | Complement (1) | A ( A |
| DATA TRANSFER INSTRUCTIONS | SC | 20 0010 0000 | Set Carry flip-flop (1) | C ( 1 |
|  | RC | 24 0010 0100 | Reset Carry flip-flop (1) | C ( 0 |
|  | SF1 | 22 0010 0010 | Set FF1 (1) | FF1 ( 1 |
|  | RF1 | 26 0010 0110 | Reset FF1 (1) | FF1 ( 0 |
|  | SF2 | 21 0010 0001 | Set FF2 (1) | FF2 ( 1 |
|  | RF2 | 25 0010 0101 | Reset FF2 (1) | FF2 ( 0 |
|  | LD | 30 – 37 0011 0xxx | Load Accumulator from Memory (1) | A ( M B(7:5) ( B(7:5) ( [I(3:1)] |
|  | EX | 38 – 3F 0011 1xxx | Exchange Accumulator and Memory (1) | A ( M B(7:5) ( B(7:5) ( [I(3:1)] |
|  | EXD | 28 – 2F 0010 1xxx | Exchange Accumulator and Memory and decrement BL (1) | A ( M B(7:5) ( B(7:5) ( [I(3:1)] B(4:1) ( B(4:1) - 1 Skip on B(4:1) = 1111 |
|  | LDI * | 70 – 7F 0111 xxxx | Load Accumulator Immediate (1) | A ( [I(4:1)] |
| * Only the first occurrence of an LDI in a consecutive string of LDI's will be executed. The program will ignore the remaining LDI's and execute the next valid instruction. |

|  | Mnemonics | I/D Bus OP Code Hex & Binary | Name (Execution cycles) | Symbolic Equation |
| --- | --- | --- | --- | --- |
| DATA TRANSFER INSTRUCTIONS (cont.) | LAX | 12 0001 0010 | Load Accumulator from X register (1) | A ( X |
|  | LXA | 1B 0001 1011 | Load X Register from Accumulator (1) | X ( A |
|  | LABL | 11 0001 0001 | Load Accumulator with BL (1) | A ( B(4:1) |
|  | LBMX | 10 0001 0000 | Load BM with X (1) | B(8:5) ( X |
|  | LBUA | 04 0000 0100 | Load BU with A (1) | B(12:9) ( A |
|  | XABL | 19 0001 1001 | Exchange Accumulator and BL (1) | A ( B(4:1) |
|  | XBMX | 18 0001 1000 | Exchange BM and X (1) | X ( B(8:5) |
|  | XAX | 1A 0001 1010 | Exchange Accumulator and X (1) | A ( X |
|  | XS | 06 0000 0110 | Exchange SA and SB (1) | SA ( SB |
|  | CYS | 6F 0110 1111 | Cycle SA register and Accumulator (1) | A ( SA(4:1) SA(4:1) ( SA(8:5) SA(8:5) ( SA(12:9) SA(12:9) ( A |
|  | LB * | C0 – CF 1100 xxxx (second word from page 3) | Load B indirect (2) (Push PC to stack, Load indirect address, Load B, Pop PC from stack) | SB ( SA ( P P(12:5) ( 0000 1100 P(4:1) ( I1(4:1) B(12:9) ( 0000 B(8:1) ( [I2(8:1)] P ( SA ( SB |
|  | LBL * | 00 0000 0000 xxxx xxxx | Load B long (2) | B(12:9) ( 0000 B(8:1) ( [I2(8:1)] |
|  | INCB | 17 0001 0111 | Increment BL (1) | B(4:1) ( B(4:1) + 1 Skip on B(4:1) = 0000 |
|  | DECB | 1F 0001 1111 | Decrement BL (1) | B(4:1) ( B(4:1) - 1 Skip on B(4:1) = 1111 |
| SPECIAL | SAG | 13 0001 0011 | Special Address Generation (1) (Contents of B remain unchanged) | A/B Bus (12:5) ( 0000 0000 A/B Bus (4:1) ( B(4:1) |
| * Only the first occurrence of an LB or LBL instruction in a consecutive string of LB or LBL will be executed. The program will ignore the remaining LB or LBL and execute the next valid instruction. |

|  | Mnemonics | I/D Bus OP Code Hex & Binary | Name (Execution cycles) | Symbolic Equation |
| --- | --- | --- | --- | --- |
| CONTROL TRANSFER INSTRUCTIONS | T | 80 – BF 10xx xxxx | Transfer (1) | P(6:1) ( I(6:1) |
|  | TM | D0 – FF 11xx xxxx (second word from page 3) | Transfer and Mark indirect (2) (Push PC to stack, jump to indirect address) | SB ( SA ( P P(12:9) ( 0000 P(8:1) ( I1(8:1) P(12:9) ( 0001 P(8:1) ( I2(8:1) |
|  | TL | 50 – 5F 0101 xxxx xxxx xxxx | Transfer Long (2) | P(12:9) ( I1(4:1) P(8:1) ( I2(8:1) |
|  | TML | 01 – 03 0000 00xx xxxx xxxx | Transfer and Mark Long (2) | SB ( SA ( P P(12:9) ( I1(4:1) P(8:1) ( I2(8:1) |
|  | SKC | 15 0001 0101 | Skip on Carry flip-flop (1) | Skip if C = 1 |
|  | SKZ | 1E 0001 1110 | Skip on Accumulator Zero (1) | Skip if A = 0000 |
|  | SKBI | 40 – 4F 0100 xxxx | Skip if BL equal to Immediate (1) | Skip if B(4:1) = I(4:1) |
|  | SKF1 | 16 0001 0110 | Skip on FF1 flag (1) | Skip if FF1 = 1 |
|  | SKF2 | 14 0001 0100 | Skip on FF2 flag (1) | Skip if FF2 = 1 |
|  | RTN | 05 0000 0101 | Return (1) | P ( SA ( SB |
|  | RTNSK | 07 0000 0111 | Return and Skip (1) | P ( SA ( SB P ( P + 1 |
| INPUT / OUTPUT INSTRUCTIONS | IOL | 1C 0001 1100 xxxx xxxx | Input / Output Long (2) | A ( Data Bus (8:5) A ( Data Bus (4:1) I2 ( I/O Device (8:5 = Device, 4:1 = Data) |
|  | DIA | 27 0010 0111 | Discrete Input Group A (1) | A ( DIA |
|  | DIB | 23 0010 0011 | Discrete Input Group B (1) | A ( DIB |
|  | DOA | 1D 0001 1101 | Discrete Output (1) (enhanced on PPS-4/2) | DOA ( A (also DIB ( X on PPS-4/2) |
| The word "skip" as used in this instruction set means the following instruction will be read from memory but not executed. Each skipped word will require one clock cycle time. Instructions ADI, LD, LDI, EX, EXD, LB and LBL have a numeric value coded as part of the instruction in the immediate field. This numeric value must be in complementary form on the bus. All of these immediate fields which are inverted are shown in brackets [ ]. |